## Slide 1: D-Star Introduction
Max Polishevsky VE6MAD
Ian Burgess VA6EMS

## Slide 2
What is D-STAR?
  Digital Smart Technology for Amateur Radio
  JARL
    Japanese Amateur Radio League
    NOT Manufacturers!
  Goal
    Advancement of the hobby
    Spectrum Efficiency
    Experiment with Simultaneous Voice and Data
  D-STAR Gateway owned by Icom
    Not Public Domain or Open Source
    May not be copied, shared or redistributed

## Slide 3
Why is D-STAR interesting?
  Spectral Efficiency
  Simultaneous Voice and Data capability
    2m/70cm/23cm
  High-Speed Data capability
    23cm
  Internet Linking capability
  Microwave Linking capability

## Slide 9
Why is D-STAR interesting?
  Spectral Efficiency
    6.25 kHz emission
    10 kHz channel spacing (reasonable)
    More efficient use of available bandwidth
    Allows more channels in crowded spectrum
    Better performance compared to analog FM
      Same power in less bandwidth (SSB vs. AM)

## Slide 10: Terminology
AMBE
  Advanced Multi-Band Excitation (AMBE) is a very powerful proprietary speech coding standard developed by Digital Voice Systems, Inc. (From: http://en.wikipedia.org/wiki/Advanced_Multi-Band_Excitation)
  Converts audio to and from the digital format used in D-Star Digital Voice at 2400 bps with 1200 bps of FEC.
FEC
  Forward Error Correction

## Slide 12
Why is D-STAR interesting?
  Simultaneous Voice and Data capability
    2m, 70cm, 23cm Digital Voice Mode
    4800bd Data Stream
      2400bd Digital Voice
      1200bd FEC on Digital voice
      1200bd Serial Data

## Slide 14: The DV Protocol
Data
Radio Header
Radio ID
Bit Synchronization 64 bits
Frame Sync
15 bits
Flag
2
8 bits
Flag 1
8 bits
Flag
3
8 bits
P_FCS
This Station Comment 32 bits/4 char
Destination Repeater Call 64 bits/8 char
Local Repeater Call 64 bits/8 char
Destination Station Call 64 bits/8 char
This Station Call
64 bits/8 char
W7SP B
W7SP A
CQCQCQ
K7VE
JOHN

## Slide 15: The DV Protocol
Data
Radio Header
Audio Frame
72 bits
Data Frame
24 bits
Final Data Frame
48 bits
Alternating Audio/Data

## Slide 16
Why is D-STAR interesting?
  High-Speed Data capability
    23cm
      128kb Ethernet
      Transparent Bridge
        Allows Network-Agnostic Applications!
      Half-Duplex
        Duplex-sensitive apps don’t work well (VOIP, etc.)

## Slide 17: The DD Protocol
Radio ID
Bit Synchronization 64 bits
Frame Sync
15 bits
Flag
2
8 bits
Flag 1
8 bits
Flag
3
8 bits
P_FCS
This Station Comment 32 bits/4 char
Destination Repeater Call 64 bits/8 char
Local Repeater Call 64 bits/8 char
Destination Station Call 64 bits/8 char
This Station Call
64 bits/8 char
W7SP B
W7SP A
CQCQCQ
K7VE
JOHN
Ethernet Style Packet
Radio Header
Length
16 bits

## Slide 18: The DD Protocol
Ethernet Style Packet
Radio Header
Length
16 bits
Data Frame
128 – 12000 bits
MAC Src Addr
48 bits
MAC Dest Addr
48 bits
Type
16 bits
FCS
32 bits
TCP/IP

## Slide 19
Why is D-STAR interesting?
  Internet Linking capability
    User linking vs. Site linking
    Can cause confusion for uninformed (example later)
    Allows “roaming”

## Slide 20
Why is D-STAR interesting?
  Microwave linking capability
    Install additional regional site(s)
    Allows extra connectivity without need for additional Gateway server or additional internet connections
    Expensive – approx $5k per and 2 needed

## Slide 21: D-Star Radio Products

## Slide 22: Icom D-STAR Controller & Repeaters

## Slide 23
Typical “Full” Stack

## Slide 24
Icom D-Star Radio Products
ID-31A
IC-80AD
IC-91AD
IC-92AD
IC-9100
ID-880AH
ID-1
IC-2820AH

## Slide 25
New Applications
  Hardware
    μSmartDigi™ D-Gate
    DV Dongle

## Slide 26: μSmartDigi™ D-Gate
Black box translator
  D-PRS ® to APRS
  APRS to D-PRS®
Smooth RF integration of both systems

## Slide 27
Fits inside a small box
Converts D-STAR NMEA GPS data to Base-91 compressed APRS® Position Reports
Converts Symbol and Text Data
Filters messages according to a rich set of user-configurable rules
Operates without a dedicated laptop or PC

## Slide 28: Third Party Products
DVRPTR Open Source Hotspot Modem
DV Acccess Point (DVAP)
(VHF Radio-to-Internet Interface)
DV Dongle
(No Radio Required)

## Slide 29: D-STAR TNC
An APRS and D-STAR software bridge
  Java Based package
www.aprs-is.net/dstartnc2.htm
DStarTNC2 is free for use by Amateur Radio operators for Amateur Radio.

## Slide 30: D-RATS Free Software
A Communications Tool For D-STAR

## Slide 31: D-RATS Forms
Includes Form Editor to Create Any Form
Only Data is Sent
Fully printable ICS-213, ARRL Radiogram and NTS Forms Included

## Slide 32: Summary
Lots of potential for use of simultaneous voice & data
Spectral efficiency offers opportunity for better utilization
Better performance from narrow spectrum & FEC
Distinct operational differences from familiar FM
New applications will drive acceptance
EmComm demand for tactical voice and data communications by served agencies

## Slide 33: VE6IPG Proposal
“Inter-connected” system (D-Star, FreeStar*, IRLP, EchoLink, VoIP, AllStar*)
Seamless reflector linking (L,U VS X,O)
RF Improvements
Will be 1 of 2 Multimode Systems Canada Wide
Emergency Prepared System

## Slide 34
VE6IPG, Calgary
DVDongle + Server
=
Multi-Mode System
FreeStar*
D-Star
IRLP
EchoLink
AllStar*
FM**
** FM Analog in the Digital World is frowned upon, but is here to demonstrate the full potential of a multi-mode system.
RF

## Slide 35: Some Useful Web Sites
www.icomamerica.com/support/forums
www.K5TIT.Org/Forum
Some D-STAR Web Sites:
http://www.d-starusers.org/
http://www.d-rats.com/
www.aprs-is.net/dstartnc2.htm